## Slide 1: HWP01
Hardware Programming
Introduction to digital systems
And structured digital design

## Slide 2: Goal of this course
Learn to describe digital circuits with VHDL and implement them in an FPGA.

## Slide 3: Instructors
Ron Verhagen VeRon@hr.nl
Harry Broeders BroJZ@hr.nl

## Slide 4: Organization
Compulsory attendance
HWP01 structure:
  Lecture
    Five lectures: Monday: 1.5 hour p/w
  Lab exercise
    Full-time: Tuesday: 2.5 hours Online p/w
  Homework
    56.5 hours total
    Theory from the book
      “Circuit Design with VHDL” (Third Edition)
      Volnei A. Pedroni
      ISBN 978-0-262-04264-2
    Preparing assignments / writing code
    Making simulations at home / outside regular class times

## Slide 5: Planning: theory
First week
  Introduction digital systems
  Introduction to FPGAs
  Structured digital Design
  Modeling concepts in VHDL
Second week
  Introduction VHDL
  Code structure
  Data types
Third week
  Combinational versus sequential design
  Concurrent and sequential code
  Signals and variables
Fourth week
  Introduction to state machines
Fifth week
  Designing state machines
  Advanced VHDL design

## Slide 6: Planning: lab assignments
Week | Deadlines | Retake
1 | - | -
2 | 1 (deadline) | -
3 | 2 (deadline) | 1 (deadline)
4 | 3 (deadline) | 2 (deadline)
5 | 4 (deadline) | 3 (deadline)
6 | 5 (deadline) | 4 (deadline)
7 |  | 5 (deadline)
8 | Final assignment | 
 |  | Retake (HT1)
In the course manual you will find instructions on submitting
your assignments.

## Slide 7: Earning your grade
 | Action | Completed
Step 1 | Complete all 5 Labs before starting on your final assignment | Yes
Step 2 | Final Assignment (FA) ingredients: | % (leerdoel)
2.1 | Architecture (schematics and drawings) with basic ** functionality | 20% (LD1)
2.2 | VHDL code of all architectural functions and justification in report | 40% (LD2,LD3)
2.3 | A functional VHDL Test Bench | 20% (LD4)
2.4 | A working FPGA prototype with the basic** functionality | 20% (LD5)
 | ** basic functionality (complexity) may be expanded to include additional features for a higher grade. This is agreed upon before starting this assignment. Basic functionality = 6 | 
HT1 | Retake | 
In the course manual you will find the the following

## Slide 8: Agenda
Introduction to digital systems and FPGAs
Structured digital design
Modelling concepts in VHDL

## Slide 9: Computing realization
Software programmed processors: software flexibility, fixed instructions and performance is limited
Application Specific Integrated Circuits (ASIC): expensive, time consuming, best performance.
Reconfigurable computing: high flexibility, good performance and fills the gap between hardware and software. This is the domain of FPGAs.

## Slide 10: Digital Logic: 1980’s vs today FPGA
Field-programmable Gate Array (FPGA)

## Slide 11: Transistor count for key FPGA families
Source: https://www.napatech.com/road-to-fpga-reconfigurable-computing/ 2018

## Slide 12: Comparison
Field-programmable Gate Array (FPGA)
Not only is the performance of FPGAs and other logic devices becoming more formidable, these devices are incorporating functions typically performed by other types of logic, CPUs, GPUs, and DSPs. They’re the semiconductor versions of the Swiss Army Knife.
Microcontrollers vs. FPGA’s
uController | FPGA
Programming languages (C, C++, Assembly) Optimized for general purpose computing | Programming Languages VHDL, Verilog, Open Computing Language; Or use Schematics
Control over the Software; 10’s to 100’s of cores. | Control over the Hardware; Hardware timed execution; millions of progammable digital logic cells.
Predefined instruction set and datapath widths | No predefined instruction set or datapath widths
Reprogrammable - unlimited | Reconfigurable - unlimited

## Slide 14: Technology
FPGA’s are designed to function like any digital component. In order to support this programability, FPGA-chips contain the following 3 building blocks:

## Slide 15: Technology – Logic Blocks A basic logic building block is the Logic Element
If we bypass the flip-flop using the multiplexer, what is the function of this Logic Element?
LUT |  |  | 
A | B | C…F | OUTPUT
0 | 0 | X | 0
0 | 1 | X | 1
1 | 0 | X | 1
1 | 1 | X | 0
Logic Element
Synthesis (programmed into the LUT)
Output

## Slide 16: Technology - Interconnections

## Slide 17: THE DE1 development BoarD

## Slide 18: Agenda
Introduction to digital systems and FPGAs
Structured digital design
Modelling concepts in VHDL

## Slide 19: Structured digital design
Determine the function you want to perform
  Architecture
Find a method to implement the function
  Implementation
Use tools to materialize the method
  Realization
Verify your design
  Simulation and evaluation

## Slide 20: Example VHDL code
1. Import the necessary libraries
2. An entity block is the beginning building block of a VHDL design.
Each design has only one entity block which describes the interface signals into
and out of the design unit.
3. Architecture block defines how the entity operates using Structural or Behavioral
Code. This example is using behavioral code.
Y

## Slide 21: From VHDL to FPGA
ENTITY inverter IS
PORT (a: IN STD_LOGIC;
b: OUT STD_LOGIC);
END inverter;
=
A
B
ARCHITECTURE voorbeeld OF inverter IS
BEGIN
b <= NOT(a);
END voorbeeld;
=
a
b

## Slide 22: Structural decomposition
Top-down design: no constraints on the availability of hardware
Bottom-up design: design is conditioned by what’s available (e.g., the number of gates)
Typical dimensions for the Digital Design Space: speed, chip area (cost), power

## Slide 23: Agenda
Introduction to digital systems and FPGAs
Structured digital design
Modelling concepts in VHDL

## Slide 24: Simplified VHDL Design Flow
Specifications
VHDL code
Analysis & Synthesis
Place and Route
Generate Programming File
Download to Physical Device
Generate RTL functional Netlist
Generate post synthesis functional Netlist
Generate post fitting Timing Netlist
RTL functional Simulation
Post Synthesis functional Simulation
Post fitting Timing Simulation
SYNTHESIS
Whatever the final circuit inferred from the code is,
Its operation should always be verified by means of
Simulations.

## Slide 25: Modeling concepts in VHDL
Two abstract models to describe your design in VHDL
Behavioral Model:
  Less specific about how digital function(s) will actually be connected together.
  Register Transfer level (RTL): synthesizable, has an explicit clock
  Algorithmic level: (almost always) unsynthesizable, especially when there is no notion of a clock and no delays between internal functions are defined.
Structural Model:
  Gate level: oldest digital logic design method. You, the designer, do all the work.
  Wider use of “portmap”

## Slide 26: Modeling abstractions
Figure adapted from VHDL Design Representation and Synthesis.

## Slide 27: From VHDL to FPGA
Synthesize
  Simulate (Analysis & Elaboration)
  Compiles code into RTL (Register Transfer Level) schematic. Always take a look at this
Specifications
VHDL code
Analysis & Synthesis
Place and Route
Generate Programming File
Download to Physical Device

## Slide 28: From VHDL to FPGA
Place and Route
  How to configure the FPGA elements to become the functional equivalent of the RTL schematic?
  Find the optimal paths through the FPGA
  Timing analysis
Generate bitstream
  Contains the setting of every switch in the FPGA
Specifications
VHDL code
Analysis & Synthesis
Place and Route
Generate Programming File
Download to Physical Device
...to behave like this?
Place and Route
How to get this ...

## Slide 29: Design verification
Check if your realization matches your expectations.
In VHDL we use test benches to verify the results.
In this course you will create test benches to verify your designs.
In (simple) simulations we don’t know if the actual design meets timing constraints. We will discuss this later.

## Slide 30: Homework
Covered today:
  Introduction to digital design and FPGAs
  Structured design
  Modeling concepts in VHDL
Team up with another student
Start working on the laboratory
https://nandland.com/fpga-101/
https://fpgatutorial.com/vhdl/
Useful:
  Chapter 5 “Introduction to VHDL”
  Chapter 6 “Code Structure and Composition”
Next week (for reference):
  Chapter 7 and 8 “Datatypes”
  Chapter 9 “Operators”
  Chapter 18 “Introduction to Simulation with Testbenches”

## Slide 31: First week: Lab
Introductory Assignment 1
  Getting to know Quartus
  Getting to know ModelSim
  Getting to know the DE1 SoC development and Education Board